User Manual
Helmer LK503

GPS tracker & SOS communicator

Important, please attention:

1. This tracker was designed for people and asset location and communication, our company assumes no liability or responsibility for any behaviors violate other individual’s privacy.

2. Due to external factors all GPS devices have position error, so the position provide by this device just for reference only.

3. There may be delays caused by telecom operators at certain circumstance. Our company doesn’t assume liability for users’ personal and property safety

Main Features:

- GSM quad band network, all global GPS location

- Tracking Via website/IOS APP/Android APP/We chat/SMS

- Push button SOS alarm

- Click to call

- Ring tone+ Vibrate alert

- Two way Hi-Fi audio communication

- Hand-free talk

- Activity monitor

- Low battery alarm

- SIM changing alarm

Accessories

1* Main Host

1* Charger

1* Multiple-function USB cable

1* User manual

1* Necklace Style Lanyard

Product specification:

GSM network: 850/900/1800/1900MHz

GPRS standard: Class 12, TCP/IP

GPS locating time:

- 30sec with cold boot (open sky)

- 29sec with warm boot (open sky)

- 5sec with hot boot (open sky)

GPS positioning accuracy: 10-15m

Working temperature: -20℃ ~ +70℃

Working humidity: 5% ~ 95% RH

Host size: 40x34 x14mm

Host weight: 27g

Product View:

| Item | Function | Item | Function |
| --- | --- | --- | --- |
| 1 | Reboot hole | 2 | Power on/off |
| 3 | USB charger hole | 4 | Button 1 |
| 5 | GSM indicator light | 6 | SOS button |
| 7 | GPS indicator light | 8 | Button 2 |
| 9 | SIM card slot | 10 | Microphone |
| 11 | Loudspeaker | 12 | Hang rope hole |

Prepare for work:

Please choose GSM network-based Micro-SIM card (same as Iphone4) for the product. And please note:

a. Please be sure the tracker is turn off before insert or take out the Micro-SIM.b. Please be sure the GPRS and Caller id has been activated

Power on /off:

Please insert the Micro-SIM card into the card slot as directed.

Press the POWER key for 3 sec, then the tracker will ring and light on.

Indicator light show:

| Light Color | Function | Slow Flash | Fast Flash | Close |
| --- | --- | --- | --- | --- |
| Blue | GPS Indicator | GPS Searching | GPS Success | GPS Sleeping |
| Yellow | GSM Indicator | GSM Searching | GSM Success | GSM Sleeping |

APP binding and function setting:

- Scan the User manual back cover QR code to install the APP

- Enter the ID number and password to login, the default password is 123456.

- Confirm the device online, the corresponding instruction set can be achieved

- Real-time Tracking:show the last position and trace.

- Historical route:display the historical .

- Geo-fence: set and display geo-fence area,when the device get into or get out the geo-fence then it will send a alert SMS.

- Device message:display the alert list.

- Alarm setting:get the remind via APP when alarm

- Logout:logout the APP,and never get the alarm remind via APP.

- Setting

5.Answer Mode:

- Silent monitoring mode:

All have set 5 phone numbers dialing the device; you can remote listen to the voices around the device at the condition of no bell ring, but can’t speak to the device user.

- Auto answer mode:

All have set 5 phone numbers dialing the device, after a bell ring, you can remote listen to the voice around the device and speak to the user

- Push to talk mode:

Any number dialing the device number, only after the user press the button, you can speak to the device user

6.Language Setting：

Choose SMS language, the device provide three languages: Chinese, English and French

7.Do not disturb Mode:

In push-to-talk mode, whether to allow incoming strange number.

8.Time zones：

The factory default is UTC+08:00; users can set it according to local time zone.

Please log on http://www.gps123.org to learn more details of APP and platform

All functions also can set by SMS command

All command use in lowercase letters, without any blank space and ending by #.

Command for setting master number:

password,sos1,phone number#

For example:123456,sos1,180********#

The tracker will reply: 180******** has been set for the master number successfully.

Note:All SMS setting must send via SOS1 number.

| Command | Function |
| --- | --- |
| password,t,password | Change the password, factory default is 123456. |
| password,sos1, number# | Set master number |
| sos2(3,4,5), number# | Set sos2 number |
| callvib,1# | Turn on vibrate alert (factory default） |
| callvib,0# | Turn off vibrate alert |
| aj# | Set push to answer incoming call (factory default) |
| mt# | Auto-answer and hand free incoming call |
| jy# | Silence monitoring |
| dw# | Check the position |
| dsp# | Check the device work situation |
| lag,1# | Change the language to Chinese(factory default) |
| lag,2# | Change the language to English |
| lag,3# | Change the lauguage to French. |
| tim,digital# | Setting interval of the position data uploadthe unit is minutes |
| gon# | Turn on the tracking function(factory default) |
| goff# | Turn off the tracking function |
| lon# | Turn on the Indicator light (factory default) |
| loff# | Turn off the indicator light |
| dndoff# | Turn off DO NOT DISTURB in push-to-talk mode (factory default) |
| dndon# | Turn on DO NOT DISTURB in push-to-talk mode |

Command for SMS setting

Remark:

1. The tracker will boot automatically when it was charging.

put the tracker in network signal better position when use.

2. The new machines need to be recharged for 2-3 hours before use in order to achieve the best results, please use our distribute charger avoid damage to the host.

3. Standby time:

1) Upload location data every 10 minutes, the standby time is 50 hours, talking time is 5-8 hours (Actual test)

2) Turn off GPRS, the standby time is 300 hours, about 12 days .

Note: Above test data is under the status of strong GSM network

- Please charging and boot with SIM card, the device will automatically reboot when it can’t search GSM network.

- This product is not waterproof, please pay attention when using.

- GPS data upload time interval,factory default setting:10 minutes.

FAQ

Q: After inserting a SIM card, it can make a call, but it display not enable on the platform and APP

A: Please check that SIM Card has opened GPRS.

Q: In the DO NOT DISTURB mode, why any phone can call in?

A: Please check that SIM Card has opened caller ID.

Q: Device show online, but it shows “wait for the device responses” when you set instruction with APP.

A: a. Device signal is not good, so not smooth result of GPRS

b. Device is busy.

Q: The SIM card has opened GPRS function, but the device still not online

The tracker have pre-program all most APN, maybe the

APN of the SIM card you use don’t preset in the tracker,  please set SOS1 number first and then send command to add you APN into the tracker.

The command is: anp,<apn>#

# Text boxes

1.Locate interval: set the location data upload density, shorter standby time according to shorter interval.

2.SOS1 phone number: Button 1 phone number, also the master phone number, used to send command and receive alarm.

3.SOS2 phone number: Button 2 phone number, when you press button 2, the device will call the phone number.

4.White list number: the othe SOS number, also allow to remote listening