。GPS tracker＆power bank
      Helmer LK 510

Important, please attention:

1. This tracker was designed for people and asset location, our company assumes no liability or responsibility for any behaviors violate other individual’s privacy.

2. Due to external factors all GPS devices have position error, so the position provide by this device just for reference only.

3. There may be delays caused by telecom operators at certain circumstance. Our company doesn’t assume liability for users’ personal and property safety.

Main features:

- GSM quad band network, all global universal.

- Tracking Via website/IOS APP/Android APP/Wechat/SMS

- Trajectory playback /Geo-fence

- Magnetic sensor/vibration sensor/sound sensor, three types of anti-theft alarm

- Power bank/LED flashlight

- One month standby time

- High frequency buzzer alarm

- Voice monitor

- Low battery alarm

- SIM card changing alarm

Product specification:

GSM network: 850/900/1800/1900MHz

GPRS standard: Class 12, TCP/IP

GPS locating time:

- 30sec with cold boot (open sky)

- 29sec with warm boot (open sky)

- 5sec with hot boot (open sky)

GPS positioning accuracy: 10-15m

Working temperature: -20℃ ~ +70℃

Working humidity: 5% ~ 95% RH

Dimension: 12.2*5.1*2.5cm
Weight: 130g

Input: DC5V=2A

Output: DC5V=2A
Capacity: 4500MA

Accessories

1* Main Host

1* USB charger

1* Magnet box

1* User manual

1* Holder

Product view:

Prepare for work:

- Use the product as a power bank: Please charge the power bank or use the power bank charge the other electronic products as the illustration.

- Please pay attention to the battery indicator lights zone,4 lights on means full power, one light means low battery, when charge the other electronics, if just one light on, please charge the power bank first.

- Use the product as a GPS tracker :Please choose GSM network Micro-SIM card (same as Iphone4) for the produc, and be sure the GPRS data and caller ID has been activated.

Power Button instruction

1.Power on /off GPS tracker

1. Please insert the Micro-SIM card as the instruction.(Be sure the GPS is power off)

2. Press power key for 3-5 seconds, power on. (With three gentle buzzer sounds)

3. Press power key for 3-5 seconds, both of the blue and yellow lights are lightening for 15 seconds and then lights out, power off successfully.

| Light Color | Function | Slow Flash | Fast Flash | Close |
| --- | --- | --- | --- | --- |
| Blue | GPS Indicator | GPS Searching | GPS Success | GPS Sleeping |
| Yellow | GSM Indicator | GSM Searching | GSM Success | GSM Sleeping |

2.Flashlight function

Click the power key, the flashlight will on or off.

GPS function instruction :

APP binding and function setting:

- Scan the QR code on the user manual cover or search the ‘AnyTracking’ in IOS store or Google play store to install the App.

- Enter the ID number and password to login, the default password is 123456.

- Confirm the device online, then you can set the device on APP.

- Real-time tracking: show the last position and trace.

- Historical route: display the historical.

- Geo-fence: set and display geo-fence area, when the device gets into or get out the geo-fence then it will send a alert SMS.

- Device message: display the alert list.

- Alarm setting: get the remind via APP when alarm

- Logout: logout the APP, and never get the alarm remind via APP.

- Setting (set the GPS and alarm funtion)

7. Alarm Mode:

- Only APP: When there is an alarm, only through the APP alarm. If you don’t login app, it can’t receive alarm prompt.

- SMS, phone and APP: when there is an alarm, all three kinds notice. (will produce corresponding SMS messages and phone cost)

- Phone and APP: when alert occurs, first call and then APP notifications. (If the phone will produce cost).

- SMS and APP: when alert occurs, SMS alarm and APP notifications. (Will produce SMS cost )

8. Buzzer alarm: Open or close product high-frequency buzzer alarm.

9.Language Setting：

Choose SMS language, the device provide three languages: Chinese, English and French

10.Time zones：

The factory default is UTC+08:00; users can set it according to local time zone.

Please log on www.gps123.org to learn more details of APP and platform

All functions also can set by SMS command

All command use in lowercase letters, without any blank space and ending by #.

Command for setting master number:

password,sos1,phone number#

For example:123456,sos1,180********#

The tracker will reply: 180******** has been set for the master number successfully.

Remark:

1.The tracker will boot automatically when it was charging.

put the tracker in network signal better position when use.

- The new machines need to be recharged for 8 hours before use in order to achieve the best results, please use our distribute charger avoid damage to the host.

3.Standby time:

1) Upload location data every 10 minutes, the standby time is 30 days, talking time is 60-80 hours (Actual test).

2) Turn off GPRS, the standby time is 3 months.

Note: Above test data is under the status of strong GSM network

4. When use the product, in order to avoid to reduce the battery life, please do completely discharge full charge cycle operation once every three months. In use process, if the brightness of the LED lights is very weak, the battery in a state of completely discharges. In order to protect the battery, should stop to use, must be timely to recharge.(in this case, do not use while charging, otherwise the battery is easy to loss)

5. This product is not waterproof, please pay attention when using.

FAQ

Q: After inserting a SIM card, it can make a call, but it display not enable on the platform and APP.

A: Please check that SIM Card has opened GPRS.

Q: In the DO NOT DISTURB mode, why any phone can call in.

A: Please check that SIM Card has opened caller ID.

Q: Device show online, but it shows “wait for the device responses” when you set instruction with APP.

A: a. Device signal is not good, so not smooth result of GPRS;

b. Device is busy.

Q: The SIM card has opened GPRS function, but the device still not online.

The tracker have pre-program all most APN, maybe the

APN of the SIM card you use don’t preset in the tracker,  please set SOS1 number first and then send command to add you APN into the tracker.

The command is: anp,<apn>#

Note: All SMS setting must send via SOS1 number.

| Command | Function |
| --- | --- |
| password,sos1,phone number# | Set master-control phone number |
| sos2(3,4,5), phone number# | Set sos2(3,4,5) phone number |
| don# | Turn on the door sensor alarm |
| doff# | Turn off the door sensor alarm |
| von,number# | Turn on the vibrating sensor burglar alarm( level 1 is the most sensitive and level 4 is the least sensitive) |
| voff# | Turn off the vibrating sensor burglar alarm |
| non# | turn on the sound sensor burglar alarm |
| noff# | turn off the sound sensor burglar alarm |
| ntim,number# | Set the sound sensor burglar alarm lasting time |
| mod,number# | Set the method of burglar alarm,1phone calls&messages,2only phone calls,3only messages |
| hon# | Turn on the horn remind when alert |
| hoff# | Turn off the horn remind when alert |
| dw# | Inquiry positioning by SMS message |
| dsp# | Inquiry tracker’s situation |
| gon# | Turn on the APP and web platform function .(factory default) |
| goff# | Turn off the APP and web platform function. |
| lag,number# | Change the SMS remind language , 1 is Chinese ,2 is English,3 is French. |
| lon# | Turn on the indicator light(factory default) |
| loff# | Turn off the indicator light |
| Password,t,password# | Change the password, the factory default password is 123456 |

# Text boxes

- Device info: check and mark the device information.

2.Change password: change the App and web login password.

3.Locate interval: set the location data upload density, shorter standby time according to shorter interval.

4.SOS1 phone number: button 1 phone number, also the master phone number, used to send command and receive alarm.

5.White list number: the other SOS number, also allow to remote listening.

6.Arm/Disarm: open or close related sensor alarm function.Smart door has three sensors ,can work at the same time;

- Magnetic sensor:when door open/close,it will alarm.

- Vibration sensor:when the device detect trembled,it will alarm.

- Sound sensor:when the device detect the abnormal sound, it will alarm.