USER MANUAL

330 Yard Rechargeable Electronic Remote Training Collar with

100 Level of Vibration & Shock, LCD display

◎Controller

◎Features

1.100 levels of vibration.

2.100 levels of static(optional).

- The levels can be altered by use of up & down button.

- A tone button activates a tone on the receiver collar.

- The system can be used for 1 or 2 receiver’s collar.

POWER SAVING

- The Receiver Collar will TURN OFF if is unused for 4 minutes.

- Any movement will activate the Receiver Collar into STANDBY MODE.

- The Controller will go into STANDBY MODE if there is no operation after 20 seconds and turn off after 2 minutes.

◎Getting charge

1. Charge the controller

Connect the charger connector to the charging jack.  After plugging the charger into a standard outlet， the red LED light inside the controller will be lighted. Charge the controller at least 6 hours for the first charge. After fully charged, the red LED light will be turned off automatically.

2. Charge the receiver collar

After plugging the charger into a standard outlet, the red LED light inside the receiver collar will be lighted. Charge the receiver collar at least 6 hours for the first charge. After fully charged, the red LED light will be turned off automatically.

Low battery indicator: the symbol will show up on the right down side of LCD screen.

Note:

- Charging plug needs to insert into the charging port vertically. Don’t insert it in skew angle. Otherwise it will cause damage or poor contact of charging interface.

- This is not included charger. Please charge the collar or remote by your laptop or mobile charger. The charger you select should be 5V0.5A-5V1A. DO NOT select the charger which is over 5V1A. Otherwise it is damaged the collar or remote!!

3. Then press the Y button of controller immediately and you can hear a “beep” again. That shows the item is paired successfully. If not, please press the Reset button of collar and turn it on again, and try the above steps.

Matching the second collar

If you have another collar, please follow the next steps to finish matching.

1. Please press the MODE button of controller for 5-10s, then the controller will be turned on. Press the CHANEL button  and select CHANNEL 2 (the small icon  can be seen at the upper right of the LED screen).

2. Press the reset button with paper clip for 5s within 20 seconds. While finish, you will hear a sound “beep”.

3. Then press the Y button of controller immediately and you can hear a “beep” again. That shows the item is paired successfully. If not, please press the Reset button of collar and turn it on again, and try the above steps.

Note: CHANNEL 1 and CHANNEL 2 are in no order, so you can set any collar to any CHANNEL according to you custom.

◎Intensity Regulation

The shock and vibration function can be set from 0 to 100 by pressing the UP/DOWN buttons on right hand side. When using shock or vibration, you can choose intensity levels according to your needs.

◎Using The Four Models (after encoding is completed)

Four modes can be altered by pressing the MODE button of controller.

◎Install the receiver’s contact points

According to the size of the dog and dog hair length, choose the right column for your dog between the tall one and short one.

◎How to Test Static Shock Function (after encoding is completed)

1. Take out the test bulb from the package and put it on the Receiver collar’s contact points.

2. Press Mode button of Remote controller, switch to Shock Mode, confirm LCD display not to be 0, you can press UP/DOWN button on the right side to adjust.

3. Test the Training System

The following methods will help you ascertain whether this training system functions properly. Please make sure that the remote and the receiver collar have been synced successfully.

4. Test the static shock function

•Take out the test bulb from the package and wind its metal wire on the Receiver collar’s contact points.

• Pressing the Mode button switch to Shock mode, confirm LCD display not to be 0 , and then press the UP/DOWN button to adjust the intensity level.

• Press the Y button and the test bulb will flash, that means Shock function works.

5. Test the vibration function

•Press Mode button of controller, switch to Vibrate Mode, confirm LCD display not to be 0, and then press the UP/DOWN button to adjust the intensity level.

•Press Y button, Receiver collar will vibrate, that means Vibration function works.

6. Test the beep function

•Press Mode button of Controller, switch to Beep Mode.

•Press the Y button and receive collar will beep, that mean Beep Function works.

7. Test the LED Light function

•Press Mode button of Controller, switch to Beep Mode.

•Press the Y button and then the receiver collar will flash, signifying that the LED Light function works.

Thread the collar strap through the slots on the receiver, and tie it to the dog.

Notes for use:

- The life time of the batteries vary according as how often you use the        product. Therefore you should often check the batteries by hearing the beep from the Receiver Collar and watching the indicator sign on the LCD screen of the Controller.

- The valid distance of Controller means the straight-line distance between the Controller and the Receiver Collar without obstacles in between. If there are interference signals or signal screening around, the actual remote Controller distance may vary.

- This product is for pet training. Only by training, the pet can understand the   intention of its owner. Good effect can only be achieved after a period of      training.

- Training sessions should be kept positive and short, about 10-15 minutes long each time.

- Presently, this product is the most effective and safest tool for training        pet. Following the correct operational instructions, you can effectively train the  pet and bring it no harm.